ClyPub = Unilateral counting of all pubescent setae of sizes greater than 10 µm from the front edge of the clypeus. Counting starts from the sagittal plane of the tentorial pit (a cuticular sinking in the form of points at the posterior edge of the clypeus, S280) and ends at the lateral end of clypeus. Divide the number obtained from both side of the clypeus by two.
Clypset = Presence of determinant ranges of chaetae on the clypeus. The significance of numbers 1 to 5 is indicated by following distribution pattern:
1: Setae present at the most at the front end of the clypeus or totally absent;
2: -in addition- presence of withdrawn setae at the post-apical position, around the anterior border of the clypeus;
3: furthermore, presence of one or a few chaeta(e) in a third plane a little further back;
4: thus, the presence of some chaetae in the most posterior regions of clypeus (Planes 4 and 5);
5: clypeus with detached chaetae scattered all over its surface.
CS Arithmetic mean of CW and CL
CUHL greatest length of setae on the rear side of the head.